## Slide 1
Climate Science and the Carbon Cycle
Lessons 11 to 14

## Slide 2: Lesson 11: Better than trees: solar panels for food and textiles
What role do plants play in food and fibre production?
Can we produce food and fibres more efficiently without plants by using chemical processes that use CO2, and H2O, and electricity from solar panels?
What are the challenges associated with doing this?

## Slide 3: Lesson 11: Better than trees: solar panels for food and textiles
Solar panels and trees both directly harness photons from the Sun.
In this lesson we will discover how they can provide some of our basic needs: food and textiles.
The lesson celebrates the spectacular properties of solar panels and the way they can revolutionise everything including production of food and fibres.
Optional activities are a) a toy solar panel with Nerf gun darts and table tennis balls and b) a 100W, 12V solar panel connected to a 12V electric drill, lights, fans and an electrolyser to allow students to experience renewable energy at a level relevant to actual energy use.
Notes: Solar panels and trees are analogous: they directly harness photons from the Sun. In this lesson we will discover how they can provide some of our basic needs: food and textiles.
This lesson celebrates the spectacular properties of solar panels and the way they can revolutionise everything. They can save the clearing of forests and allow marginal farmlands to be turned back into rich habitats. They can let us make foods and textiles in deserts where trees will not grow and agriculture is impossible. In addition, solar panels can power fresh water desalination, power mines, refine metals and provide the energy to make more panels and recycle old ones.
This lesson explores the ways that a world, electrified by solar panels and other forms of renewable energy, can eliminate our unsustainable demands on the Earth, with special focus on food and fibres.
Optional activities are a) a toy solar panel with Nerf gun darts and table tennis balls and b) a 100W, 12V solar panel connected to a 12V electric drill, lights, fans and an electrolyser to allow students to experience renewable energy at a level relevant to actual energy use.

## Slide 4: Lesson 11 learning intentions
At the conclusion of the lesson we will:
Harnessing of hydrogen oxidising bacteria (HOBs) is an example of how we might transform food production, bypassing photosynthesis to make protein directly from CO2 and sunlight.
Enzymes are molecular machines that can assemble CO2 into carbon-oxygen chains such as cellulose, bypassing photosynthesis and animals in the making of textiles for clothing.
Solar panels have an efficiency that greatly exceeds that of photosynthesis, providing new opportunities for reducing human impact on the biosphere.

## Slide 5: Lesson 11: Better than trees: solar panels for food and textiles
1. Review knowledge of solar panels and discuss their efficiency
2. Review photosynthesis knowledge and compare its efficiency with that of solar cells.
3. Undertake two case studies, making synthetic protein and fibres, and compare Solein and synthetic meat.
4. Review key ideas, highlighting opportunities

## Slide 6: Introduction: Solar panels and trees
Discovery of the PV effect Silicon solar cells were invented in 1954 and were about 6% efficient.
Improvements have seen efficiency of rooftop solar panels increase to 20 - 24%.
https://www.nrel.gov/news/detail/program/2022/popular-nrel-cell-efficiency-chart-shines-in-new-interactive-version#:~:text=The%20Best%20Research%2DCell%20Efficiency%20Chart%20stands%20out%20as%20being,NREL%20has%20in%20its%20records.
Research shows new materials and manufacturing may see efficiencies increase to 40 to 50%.
Notes: The photovoltaic effect is a process that generates voltage or electric current in a photovoltaic cell when it is exposed to sunlight. It is this effect that makes solar panels useful, as it is how the cells within the panel convert sunlight to electrical energy. The photovoltaic effect was first discovered in 1839 by Edmond Becquerel. When doing experiments involving chemical cells he noted that the voltage of the cell increased when its silver plates were exposed to the sunlight. (https://energyeducation.ca/encyclopedia/Photovoltaic_effect)
Briefly discuss the discovery of the photoelectric (PV) effect and various PV technologies.
Silicon solar cells were invented in 1954 and were about 6% efficient. Since that time, many improvements have been made and the typical efficiency of solar panels used on rooftops and in solar ‘farms’ is 20 to 24%.
Research shows that newly developed materials and manufacturing techniques may see efficiencies increase to 40 to 50%.

## Slide 7: Activity 1: Toy solar panel
A toy solar panel can help explain how photovoltaic cells produce electricity.
Using a cardboard box to represent different energy levels of electrons in silicon atoms, Nerf gun darts as the analogue for photons and a paddle wheel as a toy electric motor.
https://youtu.be/IgwXg2VyW1s
Source: https://www.researchgate.net/figure/Schematic-of-the-basic-structure-of-a-silicon-solar-cell-Adapted-from-22_fig1_312225770

## Slide 8: Photosynthesis
What do you remember?
Brainstorm key points.

## Slide 9: Physics and Chemistry of Photosynthesis
Photons
Carbon dioxide
CO2
Plants ‘eat’ CO2 and water helped by chloroplasts and energy carried by photons from the Sun.

## Slide 10: Photosynthesis
What do you remember?
Watch the introductory video that explains how plants produce starches and cellulous.
https://www.youtube.com/watch?v=y6gPQoO9Q4I
Watch the video
https://youtu.be/vBpsHAxsxAg
What is the key take-away from the video?
Notes: The first video reviews how plants use carbon dioxide and water to make glucose, then string them together to make the polysaccharide, or starch, which is ideal as an energy store for both plants and animals. It then shows how plants can use glucose to make a similar, but significantly different, polysaccharide called cellulose, which has very different properties to starch. These properties are examined, and appreciated for their various uses, both in nature and for humans.
The second video explains how plants and some bacteria have evolved over billions of years to trap sunlight and convert it efficiently into chemical energy. It is thought that this efficiency is achieved by exploiting a weird quantum effect called quantum coherence. Our exhibit delves into the quantum physics of photosynthesis, which may help us to generate clean power in the future.

## Slide 11: Efficiency comparison
Despite the amazing powers of nature, photosynthesis is not very efficient. Solar panels are much better.
Notes: I asked ChatGPT: What is the efficiency of energy conversion in plants storing photon energy to stored chemical energy by photosynthesis and what is the efficiency of modern solar panels energy conversion converting photon energy to electrical energy?
She came back with the following:
🌿 Photosynthesis in Plants
Process: Conversion of sunlight (photon energy) into stored chemical energy (mainly carbohydrates). Typical efficiency:
Average overall efficiency: ~1–2% under natural conditions.
Maximum theoretical efficiency: ~11% (under ideal laboratory conditions with optimal wavelengths and no losses). Explanation:
Much of the sunlight is not used — chlorophyll mainly absorbs red and blue light but reflects green and near-infrared.
Energy is lost as heat, through photorespiration, and in metabolic maintenance.
So, in the real world, only about 1–2% of the sunlight hitting leaves ends up stored as chemical energy in glucose or biomass.
⚡ Modern Solar Panels (Photovoltaic Cells)
Process: Conversion of sunlight (photon energy) directly into electrical energy. Typical efficiency:
Commercial panels: 15–23% for standard silicon-based PV cells.
High-end or laboratory multi-junction cells: 40–47% under concentrated sunlight. Explanation:
Losses occur because only part of the solar spectrum can be absorbed (bandgap limitation), and some energy is lost as heat or in resistance.
However, modern materials and multi-layer designs have dramatically improved conversion efficiency.
🔍 Summary Table
System Energy Conversion Type Typical Efficiency Theoretical Maximum
Photosynthesis (plants) Sunlight → Chemical (biomass) 1–2% ~11%
Solar panels (silicon) Sunlight → Electrical 15–23% ~33% (Shockley–Queisser limit)
Advanced PV (multi-junction) Sunlight → Electrical 30–40% ~47%
In short:
Plants: biologically elegant but energetically modest (~1–2%)
Solar panels: technologically efficient (~20–40%)

## Slide 12: Implications of having solar panels 10 to 30 times more efficient
If we could make food without the need for photosynthesis.
We could grow food with electricity and grow fibres the same way.
We could grow food in the deserts and replant farmland with forests, and we would need only one tenth of the land area to feed and clothe everyone.
This is not an idle dream, nor is it yet reality.
The first solar food factories have been built
Fibres are being grown in other factories
Many more ideas are being explored.

## Slide 13: Case Study 1: Solein
Solein food is made by growing Hydrogen Oxidising Bacteria in vats.
Water electrolysed into H2 and O2.
Bacteria feed on both H2 and CO2.
They grow by replicating and then get harvested and dried.
Uses renewable energy.
Yellow, wheat flour-like powder is the product
Notes: The process is easy to understand
Solein food is made by growing Hydrogen Oxidising Bacteria in large vats. The electrolyser turns water into hydrogen and oxygen. The bacteria feed on both hydrogen and CO2. They grow by replicating and then get harvested and dried.
Energy is provided from renewable resources.

## Slide 14: Case Study 1: Solein
Imaging the possibilities!
High end food at expensive restaurants?
Emergency food for famine-affected regions?
Protein supplements?
Integration into fast-food markets?
How might Solein be introduced?
Resistance to a new, non-agriculture-based food product?
In groups, discuss others.
Then share different group’s ideas.
Explore its carbon footprint
Ask ChatGPT to create a table showing the carbon footprint per kilogram of protein in Solein powder compared to wheat, corn, rice, beef, and cows milk.

## Slide 15: Case Study 2: Rubi changing natures way to produce cellulous
Natures way of making fabrics like cotton starts with cellulous.
Cellulose is a natural polymer, a long, repeating chain of the same molecule stuck together.
The starting point is glucose, plant food produced by photosynthesis.
The glucose molecules join in long chains to make cellulose and shed a water molecule.
Source: BBC Bitesize: https://www.bbc.co.uk/bitesize/topics/znyycdm/articles/z2d2gdm#zm33f82
Notes: The concise video clips embedded in the short BBC Bitesize website shows how plants produce cellulous. We will compare this to how a startup fabrics business are producing synthetic cellulous.

## Slide 16: Case Study 2: Rubi Laboratories and Synthetic Fibres
CO₂ is captured from industrial plants.
The CO₂ is bubbled through their reactor system
In the reactor, special enzymes turn simple carbon molecules into cellulose, the same material plants use to make their cell walls.
Rubi’s technology transforms materials production. It creates cellulose from CO₂ in just hours instead of the yearly cycle of cotton production.
This means far less water, fertilizer and land use, and less pollution.

## Slide 17: Key science ideas
Key idea 1: Solar panels have an efficiency that greatly exceeds that of photosynthesis, providing new opportunities for reducing human impact on the biosphere.
Key idea 2: Synthetic food can be made by harnessing hydrogen oxidising bacteria (HOBs), and reproducing them to make protein directly from CO2 and sunlight, thus bypassing photosynthesis
Key idea 3: Enzymes are ‘molecular machines’ that can assemble CO2 into carbon-oxygen chains such as cellulose, bypassing photosynthesis and animals in the making of textiles for clothing.

## Slide 18: Lesson 12: Turning CO2 into rock, CO2-free cement and storing carbon in the soil
This lesson will excite students and trigger them to imagine a future where revolutions in technology are allowing both farming and construction materials (concrete) to contribute to a new world where humanity and the natural world thrive together.
The key idea in this lesson is symbiosis: combining two things to make one or both better. Carbon sequestration works with carbon emitting technologies to undo the climate harm done by CO2 emissions. Students will design a city of the future called SymbioCity: all the technologies of this lesson work together, a symbiosis designed to be fully sustainable.
.

## Slide 19: Lesson 12 learning intentions
At the conclusion of the lesson, you will:
explain symbiosis in the context of climate change.
understand the concept of agrivoltaics.
create a vision of a sustainable city. be familiar with the enormous changes required to survive climate change and stabilise global warming.

## Slide 20: Lesson 12: Turning CO2 into rock, CO2-free cement and storing carbon in the soil
1. Start by reviewing and discussing the meaning of symbiosis.
2. Then apply symbiosis to agrivoltaics.
3. Learn about CO2 sequestration in rocks.
4. Learn about changing cement manufacture
5. Finish by designing SymbioCity

## Slide 21: Symbiosis
Think back to your biology lessons. What is symbiosis and what is and an example?
Can we apply this idea partnerships between technologies to increase their effectiveness?
Has anyone heard of Agrivoltaics?

## Slide 22: Symbiosis
Broad meaning: symbiosis means a close, mutually beneficial relationship between two different people, groups, or systems.
Biology meaning: describes two species living together in a way that helps one or both survive.
In everyday language, it’s used to describe any cooperative partnership where both sides gain something — for example, “a symbiosis between technology and nature” or “a symbiotic partnership between teacher and student.”

## Slide 23: Agrivoltaics
Agrivoltaics in Australia combines solar power and farming on the same land, using elevated or spaced panels to allow for crops (like horticulture) or livestock (sheep/cattle grazing) underneath, creating dual income streams, better water efficiency (less evaporation), and crop protection from harsh sun/hail, ?

## Slide 24: Silverstone: mimicking nature’s way to transform CO2 into stone
Carbfix project captures and injects CO2 deep into the ground where it reacts slowly with the minerals in these rocks, being absorbed and stored for extremely long periods.
The brief video located at: https://youtu.be/60mxSf3OPbw explains how the carbon capture and storage system works.

## Slide 25: Re-thinking cement: decarbonising cement
The world produces 4 billion tonnes of cement every year.
This produces about 8% of the world’s CO2 emissions.
Hanna Ricthie explains the current situation, describes some lower-emission alternatives, and concisely describes future decarbonisation options.

## Slide 26: Designing SymbioCity
SymbioCity is a city of the future, a city based on symbiosis.
On butchers’ paper make a plan for SymbioCity.
Location: near a large agrivoltaics plant that includes a low carbon cement plant.
The combined cement/agrivoltaics industry complex creates food, electricity and cement for a city of 1 million people.
It will use a combination of greenhouses, animals and plants growing around solar panels, ponds for ducks, free range chickens, greenhouse areas for tropical crops, sheep grazing for meat and wool.
If permitted, students can get help from AI in creating their designs.

## Slide 27: Key science ideas
Key idea 1: In science, symbiosis is a close and long-term biological interaction between two different species, where at least one of the species benefits from the relationship.
Key idea 2: This idea has been applied to Agrivoltaics where the same land is used for both farming and solar energy production. Crops are grown under or between solar panels and/or wind turbines, so the land can produce both food and clean energy at the same time.
Key idea 3: Industries such as the manufacture of cement which accounts for 8% of world greenhouse gas emissions need to be re-thought to identify zero or low-carbon emission processes to produce equivalent products.

## Slide 28: Lesson 13: Plans for a Perfect Planet
What steps should we take to create a resilient and sustainable planet that allows us to adapt to climate change and live in harmony with the natural environment?

## Slide 29: Lesson 13: Plans for a Perfect Planet
The module ends with two brainstorming sessions.
The first, ‘Plans for a Perfect Planet’, empowers everyone to imagine a perfect planet and define the plans to create it.
The second, ‘People for a Perfect Planet’ identifies the career paths that will lead to the outcomes we desire.
Notes: In this lesson, we imagine ourselves in a world where frontier technologies are in full swing; a world being repaired and transformed by human ingenuity. Farmland is being returned to forests, crops being grown in harmony with solar panels, and building construction is no longer leading to enormous carbon emissions.
But remember too, this is still the world of the climate cruise adventure. It will be a world of surprises and challenges because the CO2 we added to the atmosphere over 100 years will take a long time to be turned back into trees and wood and stone.
Plans for a perfect planet is a brainstorming session in which students create plans based on realistic innovations that could work together to make the future planet a perfect planet.

## Slide 30: Lesson 13 learning intentions
At the conclusion of the lesson, you will:
be familiar with the enormous changes required to survive climate change and stabilise global warming.
have a vision for the breadth of opportunities provided by climate change.

## Slide 31: Global plan suggestions
humans living with nature
large areas of habitat reserved for nature
net zero emissions for stabilising climate change
everyone safe from flood and fire
sea levels and ocean temperatures stabilised
space solar sunshields
neither land nor oceans over-exploited
all pollution eliminated
all materials recycled and reused.
Add other plans as students suggest alternatives.

## Slide 32: Technology plan suggestions
growing food from renewable energy in the deserts
all electric transport
clothing made from renewable energy and CO2
buildings made from renewable sustainable materials
white cities and white roads for solar energy reflection
quantum computers and AI for accurate long term weather forecasts and climate modelling
extreme weather protection
reafforestation of unsustainable farmland
forest fires extinguished by robotic drones.
Add other plans as students suggest alternatives.

## Slide 33: Brainstorming record
Use the following or similar table to record discussions and thoughts.
Global Plan | Regional Plan | Technology Plan | Benefit for the planet

## Slide 34: Key science ideas
Climate science provides an excellent example of how scientists have improved their understanding and explanations of the natural world based on evidence and that science knowledge can be changed as new insights and evidence becomes available.
We can use information from a range of sources to develop arguments about how the values and needs of society influence the focus of scientific research, and how science knowledge is used to analyse the key factors that contribute to science knowledge and practices being adopted more broadly by society.
We can establish the causal relationship between increase in atmospheric CO2 concentrations and global warming.

## Slide 35: Lesson 14: People for a Perfect Planet
What do we all need to do to create a ‘perfect plant’ where we can all live in harmony with nature and navigate the changing climate until it is stable?

## Slide 36: Lesson 14: People for a Perfect Planet
This final lesson is about our role in creating a perfect planet. The lesson begins with a presentation of the plan for a perfect planet created in the previous lesson.
We will then brainstorm careers and career paths needed for each of the technologies that ultimately underpin our creation of a perfect planet.
Finally, we drill downwards from the technologies to uncover the skill sets and the career paths available, and explore the diversity of skills needed for every exciting technology, as well as the skills needed to navigate the climate cruise adventure.

## Slide 37: Lesson 14: Learning intentions:
At the conclusion of the lesson, students will:
understand the connection between school learning and jobs in a warming world.
have a vision of how they can contribute to a better world.
recognise a diversity of career opportunities associated with reducing global warming.

## Slide 38: Lesson 14: People for a Perfect Planet
1. Review the technologies needed for a ‘perfect planet’.
2. Discuss associated career paths.
3. Consider what is needed to navigate the climate cruise adventure.
4. You imagine your own future career plan taking account of climate change and AI.

## Slide 39: Introduction
Use the following or similar table to record discussions and thoughts.
Broad area 1-10 | Specific technology | Job description | Skills and knowledge you might need | School subjects likely to be useful

## Slide 40: Key science ideas
At the conclusion of the lesson, students will:
become familiar with the enormous changes required to survive climate change and stabilise global warming.
have a vision for the breadth of opportunities provided by climate change.